## Slide 1: Introduction to hand tools
Mr. Warren

## Slide 2: Hand tool Safety
Before you use any tool, you should know how it works and some of the possible dangers of using it the wrong way.
Always read and understand the procedures and safety tips in the manufacturer’s guide for every tool you use.
Make sure every tool you use is in good condition.
Never use worn or damaged tools.

## Slide 3: Hammers
Hammers are made in different sizes and weights for specific types of work.
The safest hammers are those with heads made of alloy and drop-forged steel.
Two of the most common hammers are the claw hammer and the ball peen hammer.

## Slide 4: Claw Hammers

## Slide 5: Claw Hammers
The claw hammer has a steel head and a handle made of wood, steel or fiberglass.
You use the head to drive nails, wedges and dowels.
You use the claw to pull nails out of wood.
The face of the hammer may be flat or rounded.

## Slide 6: Claw Hammers
It’s easier to drive nails with the flat face claw hammer, but the flat face may leave hammer marks when you drive the head of a nail flush with the surface of the work.
A claw hammer with a slightly rounded face is called a bell-faced hammer.
It can be used to drive a nails flush without damaging the surface of the work.

## Slide 7: Ball peen Hammers

## Slide 8: Ball peen Hammers
A ball peen hammer is a type of hammer used in metalworking.
It has a flat face for striking and a spherical or hemispherical head for peening (rounding off) metal rivets.
You use this hammer with chisels and punches.
In welding, the ball peen hammer is used to reduce stress on the weld by peening or striking the joint as it cools.

## Slide 9: Ball peen Hammers
Ball peen hammers are also known as engineer’s hammers or machinist’s hammers.
They are classified by weight, and can weigh 6 ounces to 2 ½ lbs.
Never use a ball peen hammer to drive in nails, because the head of the hammer is made of tough, but relatively soft steel.

## Slide 10: Ball peen Hammers
Continuous pounding on nails can deform or damage the hammer’s head.
A claw hammer is not interchangeable with a ball peen hammer.

## Slide 11: Sledge Hammers

## Slide 12: SledgeHammers
A sledgehammer is a heavy-duty tool used to drive posts or other large stakes.
You can also use it to break up cast iron or concrete.
The head of the sledgehammer is made of high-carbon steel and weighs 2 to 20lbs.
Sledgehammers can be either long-handled or short-handled, depending on the jobs they are designed for.

## Slide 13: SledgeHammer safety
Wear eye protection when using a sledge hammer. It is also a good idea to wear gloves.
Replace broken or cracked handles before you use the sledgehammer.
Make sure the handle is secured firmly at the head.
Use the right amount of force for the job.

## Slide 14: SledgeHammer safety
Keep your hands away from the object you are driving.
Don’t swing until you have checked behind you to make sure you have enough room and no one is behind you.

## Slide 15: Ripping bars

## Slide 16: Ripping bars
Also called a pinch, pry or wrecking bar.
Can be 12 to 36 inches long.
Used for heavy-duty dismantling of woodwork, such as tearing apart building frames or concrete forms.
Has an octagonal (eight-sided) shaft and two specialized ends.

## Slide 17: Ripping bars
A deeply curved nail claw at one end is used as a nail puller.
An angled, wedge-shaped face at the other end is used as a prying tool to pull apart materials that are nailed together.
When using a ripping bar, make sure that you always wear the appropriate PPE and keep balanced footing

## Slide 18: Nail Pullers
Cat’s paw (also called nail claws and carpenters pincers)

## Slide 19: Nail Pullers
The cat’s paw is a straight steel rod with a curved claw at one end.
It is used to pull nails that have been driven flush with the surface of the wood or slightly below it.
You use the cat’s paw to pull the nails to just above the surface of the wood so they can be pulled completely out with the claw of a hammer or pry bar.

## Slide 20: Nail Pullers
Chisel Bar

## Slide 21: Nail Pullers
The chisel bar has a claw at each end and is ground to a chisel-like bevel (slant) on both ends.
You can use it like a claw hammer to pull nails.
You can also drive it into wood to split and rip apart the pieces.

## Slide 22: Nail Pullers
Flat bar

## Slide 23: Nail Pullers
The flat bar has a nail slot at the end to pull nails out from tightly enclosed areas.
It can also be used as a small pry bar.
The flat bar is usually 2 inches wide and 15 inches long.
To prevent injury when pulling a nail, be sure the material holding the nail is braced securely before you pull.

## Slide 24: Chisels
You will learn about two kinds of chisels in this section.

## Slide 25: Chisels
Chisels are used to cut and shape wood, stone, or metal.
A chisel is a metal tool with a sharpened, beveled (sloped) edge.
Both types are made from steel that is heat-treated to make it harder.
Can cut any material that is softer than the steel of the chisel.

## Slide 26: Chisels
Always wear safety goggles
Don’t use a chisel head or hammer that has become mushroomed or flattened.
Sharpen the cutting edge of a chisel on an oil-stone to produce a keen edge.

## Slide 27: Punches
A punch used the impact of a hammer to indent metal before you drill a hole, to drive pins, and to align holes in two parts that are mates.
Punches are made of hardened and tempered steel, and come in various sizes.

## Slide 28: Punches
The center and prick punches are used to make small locating points for drilling holes.
The straight punch is used to punch holes in thin sheets of metal.

## Slide 29: Punches
Three common types of punches are the center punch, the prick punch and the straight punch.
Prick Punch
Tapered Punch

## Slide 30: Screwdrivers
A screwdriver is used to tighten or remove screws.
They are identified by the type of screw they fit.
The most common screwdrivers are slotted (flat head) and Phillips head screwdrivers.
You may also use more specialized screwdrivers such as a clutchdrive, Torx®, Robertson®,and Allen head. (hex)
Don’t use screwdrivers near live wires

## Slide 31: Screwdrivers

## Slide 32: Pliers and Wire Cutters
Pliers are a special type of adjustable wrench.
They are scissor-shaped tools with jaws. The jaws usually have teeth to help grip objects.
You will generally use pliers to hold, cut, and bend wire and soft metals.
Do not use pliers on nuts or bolt heads. They will round off the edges of the head and wrenches will no longer fit properly.

## Slide 33: Pliers and Wire Cutters
High quality pliers are made of hardened steel
Pliers come in many different head styles, depending on their use.
They following types of pliers are the most commonly used:

## Slide 34: Pliers and Wire Cutters
Slip-joint (combination) pliers

## Slide 35: Pliers and Wire Cutters
You use slip-joint pliers to hold and bend wire and to grip and hold objects during assembly operations.
They have adjustable jaws.
There are two jaw settings: one for small materials and one for larger materials.

## Slide 36: Pliers and Wire Cutters
Long-nose (needle-nose) pliers

## Slide 37: Pliers and Wire Cutters
Long-nose pliers are used to get into tight places where other pliers won’t reach, or to grip parts that are too small to hold with your fingers.

## Slide 38: Pliers and Wire Cutters
Lineman pliers (side cutters)

## Slide 39: Pliers and Wire Cutters
Lineman pliers have wider jaws than slip-joint pliers do.
You use them to cut heavy or large-gauge wire, and to hold work.
The wedged jaws reduce the chance that wires will slip, and the hook bend in both handles give you a better grip.

## Slide 40: Pliers and Wire Cutters
Tongue-and-groove (CHANNELLOCK®) pliers

## Slide 41: Pliers and Wire Cutters
Tongue-and-groove pliers have serrated teeth that grip flat, square, round, or hexagonal objects.
You can set the jaws in any of five positions by slipping the curved ridge into the desired groove.
Large tongue-and-groove pliers are often used to hold pipes, because the longer handles give more leverage.

## Slide 42: Pliers and Wire Cutters
Locking pliers (Vise-Grip®)

## Slide 43: Pliers and Wire Cutters
Locking pliers clamp firmly onto objects the way a vise does
A knob in the handle controls the width and tension of the jaws.
You close the handles the lock the pliers, and release the pliers by pressing the lever to open the jaws.

## Slide 44: Wrenches
Wrenches are used to hold and turn screws, nuts, bolts, and pipes.
There are many types of wrenches, but they fall into two main categories: nonadjustable and adjustable.
They come in both standard and metric sizes.
Adjustable wrenches can be expanded to fit different-sized nuts and bolts.

## Slide 45: Nonadjustable Wrenches
Open-end wrench

## Slide 46: Nonadjustable Wrenches
The open end wrench is one of the easiest non adjustable wrenches to use.
It has an opening at each end that determines the size of the wrench.
Often, one wrench has two different-sized openings, such as 7/16 inch and ½ inch, one on each end.

## Slide 47: Nonadjustable Wrenches
The sizes measure the distance between the flats (straight sides or jaws of wrench opening) of the wrench and the distance across the head of the fastener used.

## Slide 48: Nonadjustable Wrenches
Box-end wrenches

## Slide 49: Nonadjustable Wrenches
Box-end wrenches form a continuous circle around the head of the fastener.
The ends have 6 or 12 points.
The ends come in different sizes ranging from 3/8 inch to 15/16-inch.
Box-end wrenches offer a firmer grip than open-end wrenches.

## Slide 50: Nonadjustable Wrenches
Box-end wrenches are safer to use than open end wrenches because they will not slip off the sides on certain kinds of bolts.
The handles of box-end wrenches are available in a range of lengths.

## Slide 51: Striking or slugging wrenches

## Slide 52: Striking or slugging wrenches
Striking or slugging wrenches are similar to box-end wrenches in that they have an enclosed circular opening designed to lock onto the fastener when the wrench is struck.
The wrenches have a large striking surface so you can hit them more accurately, usually with a mallet or handheld sledge hammer.

## Slide 53: Striking or slugging wrenches
Striking wrenches are only used in certain situations, such as when a bolt has become stuck to another material through rust or corrosion.
Striking wrenches can damage screw threads and bolt heads.

## Slide 54: Hex key wrenches

## Slide 55: Hex key wrenches
Hex key wrenches are L-shaped, hexagonal (six-sided) steel bars.
Both ends fit the socket of a screw or bolt.
The shorter length of the L-shape is called the head, and the shorter length is the handle

## Slide 56: Hex key wrenches
You might use them with setscrews.
Setscrews are used in tools and machinery to set two parts tightly together so they don’t move from the set position.

## Slide 57: Combination wrenches

## Slide 58: Combination wrenches
Combination wrenches are, as the name implies, a combination of two types of wrenches.
One end of a combination wrench is open and the other end is closed, or box-end
They speed up your work because you don’t have to keep changing wrenches.

## Slide 59: Combination wrenches
Combination wrenches are, as the name implies, a combination of two types of wrenches.
One end of a combination wrench is open and the other end is closed, or box-end
They speed up your work because you don’t have to keep changing wrenches.

## Slide 60: Adjustable wrenches
Adjustable wrenches are used to tighten or remove nuts and bolts and all types of sizes of pipes.
They have one fixed jaw and one movable jaw.
Common types include pipe wrenches, spud wrenches, and adjustable end wrenches.
They save time when working with different sizes of nuts and bolts.

## Slide 61: Adjustable wrenches
Pipe wrench

## Slide 62: Adjustable wrenches
Pipe wrenches (often called monkey wrenches) are used to tighten and loosen all types and sizes of threaded pipe.
You adjust the upper jaw of the wrench by turning the adjusting nut.
Both jaws have serrated teeth for gripping power.

## Slide 63: Adjustable wrenches

## Slide 64: Sockets and ratchets

## Slide 65: Sockets and Ratchets
Socket wrench sets include different combinations of sockets and ratchets that are used to turn the sockets.
Most sockets have 6 or 12 gripping points.
The end of the socket that fits into the handle is square.
Sockets come in different lengths.

## Slide 66: Sockets and Ratchets
The longer socket is called a deep socket.
It is used when normal sockets will not reach down over the end of the bolt and grip it
The ratchet handle has a small lever that you can use to change the turning direction.

## Slide 67: Torque wrenches

## Slide 68: Torque wrenches
Torque wrenches measure resistance to turning.
You need them when installing fasteners that must be tightened in sequence without distorting the workpiece.
You will use a torque wrench only when a torque setting is specified for a particular bolt.

## Slide 69: Torque wrenches
Torque specifications are usually stated in inch-pounds for small fasteners or foot-pounds for large fasteners.
Hold the head of the wrench with one hand to support he bolt and to make sure it is properly aligned

## Slide 70: Steel Rule

## Slide 71: Steel rule
The flat steel rule is the simplest and most common measuring tool.
Flat steel rules are usually 6 or 12 inches long, but longer sizes are available.
They can be flexible or nonflexible, thin or wide.
The thinner the rule, the more accurately it measures.

## Slide 72: Measuring tape

## Slide 73: Measuring tape
The standard tape measure blade is marked similarly to a 1/16-inch standard ruler.
Along with the ½ inch, ¼ inch, 1/8 inch, and 1/16 inch markings, the standard tape measure may also include metric increments.
The curve of the tape measure blade is designed to strengthen the blade and makes the tape easier to read when it is placed on a surface to be marked.

## Slide 74: Wooden folding rule

## Slide 75: Wooden folding rule
A wooden folding rule is usually marked in sixteenths of an inch on both edges of each side.
Folding rules come in 6 and 8 foot lengths.
Because of its stiffness, a folding rule is better for measuring vertical distance.
Unlike a tape measure it can be held straight up.

## Slide 76: Laser measuring tools

## Slide 77: Laser measuring tools
A laser measuring tool can be considered a battery powered, electronic version of a tape measure.
They work by pointing it at a specific object and then pressing a measurement button on the control panel.
When the button is pressed, a laser shoots out at the object and a reading is sent back.

## Slide 78: Levels

## Slide 79: Levels
A level is a tool used to determine both how level a horizontal surface is and how plumb a vertical surface is.

## Slide 80: Carpenter’s Square

## Slide 81: Carpenter’s Square
The carpenter’s square (framing square) is shaped like an L and is used mainly for squaring up sections of work such as wall studs and sole plates.
The carpenter’s square has a 24-inch blade and a 16-inch tongue, forming a right (90 degree) angle.

## Slide 82: Speed Square

## Slide 83: Speed Square
The speed square is another type of carpenter's square, frequently made of cast aluminum.
It is a combination protractor, try square, and framing square.
It is marked with degree gradations for fast, easy layout.

## Slide 84: Try Square

## Slide 85: try Square
The try square is a fixed, 90-degree angle and is used mainly for woodworking.
You can use it to lay out cutting lines at 90-degree angles, to check the squareness of adjoining surfaces, to check a joint to make sure it is square, and to check if a planed piece of lumber is warped or cupped.

## Slide 86: Combination Square

## Slide 87: Combination Square
The combination square has a ruled blade that moves through a head.
The head is marked with 45 degree and 90 degree angle measures.
The combination square is one of the most useful tools for layout work.

## Slide 88: Plumb bob

## Slide 89: Plumb bob
The plumb bob is a pointed weight attached to a string, uses the force of gravity to make the line hang vertical, or plumb.
When the weight is allowed to hang freely, the string is plumb.
A plumb bob can also show what point on the floor is directly under the section of the beam you need to support.

## Slide 90: Plumb bob
The plumb bob is a pointed weight attached to a string, uses the force of gravity to make the line hang vertical, or plumb.
When the weight is allowed to hang freely, the string is plumb.
A plumb bob can also show what point on the floor is directly under the section of the beam you need to support.

## Slide 91: Chalk lines

## Slide 92: Chalk lines
A chalk line is a piece of string or cord that is coated with chalk.
You stretch the line tightly between two points and then snap it to release a chalky line to the surface.

## Slide 93: Utility knives

## Slide 94: Utility knives
A utility knife is used for variety of purposes including cutting roofing felt, fiberglass or asphalt shingles, vinyl or linoleum floor tiles, fiberboard, and gypsum board.
You can also use it for trimming insulation.
The utility knife has a replaceable razor-like blade.

## Slide 95: Utility knives
It has a handle about six inches long, made of cast-iron or plastic, to hold the blade.
The handle is made of two halves, held together with a screw.
Models that have a retractable blade are the safest.
Place some scrap under the object you are cutting. This will protect the surface under the object.

## Slide 96: Backsaws

## Slide 97: Backsaws
The standard blade of this saw is 8 to 14 inches long with 11 to 14 tpi (teeth per inch)
A backsaw has a broad, flat blade and a reinforced back edge.
Its is used for cutting joints, especially miter joints and tenons.

## Slide 98: Compass keyhole saw

## Slide 99: Compass keyhole saw
The standard blade of the saw is 12 to 14 inches long with 7 or 8 tpi.
This saw curves quickly in wood, plywood, or wallboard.
It is also used to cut holes for large-diameter pipes, vents, and plugs or switch boxes.

## Slide 100: Coping saw

## Slide 101: Coping saw
This saw has a narrow, flexible 6 ¾-inch blade attached to a U-shaped frame.
Holders at each end of the frame can be rotated so you can cut angles.
Standard blades range from 10-20 tpi.
The coping saw is used for making irregular-shaped moldings fit together cleanly.

## Slide 102: Drywall saw

## Slide 103: Drywall saw
A drywall saw is a long, narrow saw used to cut softer building materials, such as drywall.
The blade on a drywall saw has a very sharp point, so that you can easily poke a hole to start your cut without drilling a starter hole.

## Slide 104: hacksaw

## Slide 105: hacksaw
The standard blade of this saw is 8 to 16 inches with 14 to 32 tpi.
It has a sturdy frame and a pistol-grip handle.
The blade is tightened using a wing nut and bolt.
Hacksaws are used to cut through metal, such as nails, bolts, or pipe.

## Slide 106: hacksaw
When installing a hacksaw blade, be sure that the teeth face away from, not toward the saw handle.
Hacksaws are designed to cut on the push stroke, not on the pull stroke.
Brace yourself when sawing so you are not thrown off balance on the last stroke.

## Slide 107: handsaw

## Slide 108: handsaw
The standard blade of this saw is 26 inches long with 8 to 14 tpi for a crosscut saw and 5 to 9 tpi for a ripsaw.
The crosscut saw is designed to cut across the grain (the direction of the fibers) of wood.
The ripsaw is designed to cut with the grain(parallel to the wood fibers) of wood.

## Slide 109: Files and rasps

## Slide 110: Rasp-cut file
The teeth are individually cut; they are not connected to each other.
They give a very rough surface.
Used mostly on aluminum lead, and other soft metals to remove waste materials.
Also used on wood.

## Slide 111: Single-cut file
Has a single set of straight-edged teeth running across the file at an angle.
Used to sharpen edges, such as rotary mower blades.
After using any file, brush away any filing with a file card

## Slide 112: double-cut file
Two sets of teeth crisscross each other.
Types are bastard(roughest cut), second cut, and smooth cut.
They are used for fast cutting.

## Slide 113: C-clamps

## Slide 114: C-clamps
This multipurpose clamp has a C-shaped frame.
The clamp has a metal shoe at the end of a screw.
Using a T-bar, you tighten the clamp so that it holds material between the metal jaw of the frame and the shoe.

## Slide 115: Locking C-clamp

## Slide 116: Locking C-clamp
This clamp works like locking pliers.
A knob in the handle controls the width and tension of the jaws.
You close the handles to lock the clamp and release the clamp by pressing the lever to open the jaws.

## Slide 117: Spring clamp

## Slide 118: Spring clamp
You use your hand to open the spring-operated clamp.
When you release the handles, the spring holds the clamp tightly shut, applying even pressure to the material.
The jaws are usually made of steel, some with plastic coating to protect the material’s surface against scarring.

## Slide 119: bar clamp

## Slide 120: Bar clamp
A rectangular piece of steel or aluminum is the spine of the bar clamp.
It has a fixed jaw at one end and a sliding jaw (tail side) with a spring-locking device that moves along the bar.

## Slide 121: Pipe clamps

## Slide 122: Pipe clamp
Although this clamp looks like a bar clamp, the spine is actually a length of pipe.
It has a fixed jaw and a movable jaw that work the same way as the bar clamp.
The movable jaw has a lever mechanism that you squeeze when sliding the movable jaw along the spine.

## Slide 123: Hand- screw clamp

## Slide 124: Hand- screw clamp
This clamp has wooden jaws.
It can spread pressure over a wider area than other clamps can.
Each jaw works independently.
You can angle the jaws toward or away from each other or keep them parallel.

## Slide 125: web clamp

## Slide 126: web clamp
This clamp uses a belt-like canvas or nylon strap or band to apply even pressure around a piece of material.
After looping the band around your work, you use the clamp head to secure the band.
A quick-release device loosens the band after you are finished.

## Slide 127: Clamps safety and maintenance
Clean and oil threads
Discard clamps with bent frames
Don’t use clamp for hoisting(pulling up) work .

## Slide 128: Chain falls

## Slide 129: Chain falls
The chain fall has an automatic brake that holds the load after it is lifted.
As the load is lifted, a screw forces fiber discs together to keep the load from slipping.
The brake pressure increases as the loads get heavier. The brake holds the load until the lowering chain is pulled. Do not get lubricant on the clutches.

## Slide 130: Come-alongs

## Slide 131: Come-alongs
Come-alongs, also called cable pullers, use a ratchet handle to position loads or to move heavy loads horizontally over short distances.
They can support loads from 1 to 6 tons.
Some come-alongs use a chain for moving their loads; others use wire ropes.

## Slide 132: Come-alongs
When using a chain come-along, use the ratchet handle to take up the chain and the ratchet release to allow the chain to be pulled out.
You can also use the fast-wind handle to take up or let out slack in the chain without using the ratchet handle.
Do not get lubricant on the clutches.

## Slide 133: shovels

## Slide 134: shovels
Shovels are used by many different construction trades.
An electrician running underground wiring may dig a trench.
A concrete mason may dig footers for a foundation.
A carpenter may clear dirt from an area for concrete form building.

## Slide 135: shovels
A plumber may dig a ditch to lay pipe.
A welder may use a shovel to clean up scrap metal and slag after the job is finished.
There are three basic shapes of shovel blades: round, square, and spade

## Slide 136: shovels
Use a round bladed shovel to dig holes or remove large amounts of soil.
Use a square bladed shovel to move gravel or clean up construction debris.
Use a spade to move large amounts of soil or dig trenches that need smooth, straight sides.

## Slide 137: picks

## Slide 138: picks
A pick is a swing tool similar to an ax.
A pick consists of a wooden handle that is 36 to 45 inches in length, and a forged steel head that can weigh between 2 and 3 pounds.
Depending on the size and strength of the pick, it can be used to break hardened or rocky soil, to level out stones and pavers, to chop tree roots and loosen soil, and to break up stones and concrete.

## Slide 139: Picks
Always check to ensure that the head is fixed firmly to the handle.
Be sure to wear appropriate eye protection
Always use a pick that is of the appropriate length and weight for your size.